## Slide 1
Profitable Growth B3X
Number one to the customer!
LG6400 Upgrade Guide.
Important Information & Instructions :
LG6400 having QSC6020 Chipset
Software to be upgraded using LGDPv1.3.9.10
Software to be upgraded in USB mode by using the
Micro USB Cable SGDY0014302 OR BJAY0023711
Upgrade Procedure :
Step 1: Install LGDPv1.3.9.10
Step 2: Install USB Modem driver
LGUSBModemDriver_WHQL_Eng_Ver_4.9.
7_All_Win7_LGEAll_CDMA.exe
Note: Old USB Modem driver (LGUSBModemDriver_Eng_Ver_4.5.1.exe) will also support this model.
Part Code  SGDY0014302
Step 3: Check USB Comport available for use.
Notes: <number>

## Slide 2
Profitable Growth B3X
Number one to the customer!
Select the Binary and Script file from C:\LG Electronics\LGDownload\Model\LG6400
LG6400 Upgrade Guide.
Notes: <number>

## Slide 3
Profitable Growth B3X
Number one to the customer!
SPC will be available on LG Mobiles site and can taken on the basis of MEID no.
LG6400 Upgrade Guide.
Notes: <number>

## Slide 4
Profitable Growth B3X
Number one to the customer!
LG6400 Upgrade Guide.
Notes: <number>

## Slide 5
Profitable Growth B3X
Number one to the customer!
LG6400 Upgrade Guide.
Notes: <number>

## Slide 6
Profitable Growth B3X
Number one to the customer!
LG6400 Lock Code Reading .
Step1 : Complete NV Edit by entering SPC
Step2 : Exit from NV Edit Screen
Step3 : Click on LOCK CODE
Notes: <number>

## Slide 7
Profitable Growth B3X
Number one to the customer!
LG6400 Multimedia File Structure.
This model doesn’t scan Multimedia files automatically. So multimedia data should be
Copied on Micro SD Card in specific Folder as shown below :
MP3 files => G:\USER\MP3\
Image files => G:\USER\IMAGE\
Video files =>G:\USER\VIDEO\
Notes: <number>