## Slide 1: SGH-S500 Dumper
Version 3.2
SAMSUNG ELECTRONICS

## Slide 2: BEFORE DUMP OR ERASE FLASH
Turn off the mobile phone
Connect download cable
Run SGH-S500 Dumper 128M program
Set com port & baud rate

## Slide 3: DUMP FLASH MEMORY
Click Start Address and select address in the Start Address window.
Select End Address.
Click START button and press power-on key of the mobile.
dump.txt is created in this program directory ( ex)C:\SGH-S500 dumper 128M V3_2\dump.txt )
Rename dump.txt because new dumped file is also concatenated in this file.

## Slide 4: ERASE FLASH MEMORY
Click ERASE and ERASE FLASH
Flash Eraser window appears
Choose Erase all the flash(All Flash Erase) or Erase the selected range(Selective Erase)

## Slide 5: ERASE All AREA
Set Select Mode as All Flash Erase (default)
Click START button and press power-on key of the mobile.
Erase Address shows the status of erasing.

## Slide 6: ERASE SELECTIVE AREA
Set Select Mode as Selective Erase
Click Start Address and select address in the Start Address window.
Select End Address.
Click START button and press power-on key of the mobile.