## Slide 1: ETS2258 Product and Maintenance Training
2007-06-19
Huawei Terminal Service Team – India

## Slide 2
Preface
HUAWEI ETS2258 is a CDMA FWT with multi-function ,handsome and gentler in appearance.
It provides voice and SMS, as well as data service.
It’s an ideal choice for family communication.

## Slide 3: Learning Guide
This course covers ETS2258 product features, technical specifications, functions , maintenance and guide, etc.
The emphasis are maintenance and guide.

## Slide 4
Chapter 1 Product Overview
Chapter 2 Technical Specification
Chapter 3 Functions Instruction
Chapter 4 Maintenance and Guide
Contents

## Slide 5: Product Overview
HUAWEI Model name: ETS2258(Reliance)
Reliance Model name:
Classic 2258

## Slide 6: Main Features
Supporting the standard CDMA2000 1X RTT.
Supporting data service.
Supporting high-quality voice services (8 kbps EVRC).
Supporting emergency call services and multiple supplementary services: caller number identification presentation, call transfer, call forwarding, call waiting, call hold and three-way calling.
Supporting phone lock;
Supporting long distance call lock.

## Slide 7: Main Features
Supporting IP telephone: storing the account number and password of IP card and implementing automatic IP dialing. For the long distance call, pre-dialing IP number automatically;
Supporting DTMF secondary dialing;
Supporting user’s individual volume settings (including handset, hand-free and ring);
Providing standard TNC antenna interface that can be connected to the indoor or outdoor antenna;

## Slide 8
Contents
Chapter 1 Product Overview
Chapter 2 Technical Specification
Chapter 3 Functions Instruction
Chapter 4 Maintenance and Guide

## Slide 9: Hardware Specification
Item | Description
Technical standard | CDMA2000 1X RTT
Frequency band | ETS2258：800M
Max transmit power | >23dBm
Max input power | -25dBm
Receiving sensibility | > -104dBm
Dimensions （W×D X H） | 214 mm × 156 mm × 77 mm
Weight | <700 g（spare battery included）
Typical power consumption | Typical power consumption during a call：1.2W Typical standby power consumption: 40mW

## Slide 10: Hardware Specification
Item | Description
Power supply | Linear power supply： AC：190V~300V DC：12V DC
Spare chargeable battery | Type：NiMH，3.6V 1000mAh
 | Max calling duration: 3hours, Max standby duration: 100hours
LCD display | LCD Module, Graphics 128*64 With ICON Y/G, STN
Temperature | Working：-10℃ ~ +55℃ Storage：-20℃ ~ +70℃
Ambient relative humidity | 5%~ 95%

## Slide 11: Hardware Specification
Item | Description
External Interface | Serial data interface: DB9（Female), for maintenance and data service.
 | Antenna: TNC（Male), connected to indoor or outdoor antenna
 | Power interface：single pin connector；
Data Cable | Maintenance Cable: Serial Port Cable,2m,D9M Data Service Cable: Serial Port To USB Cable,1.5m,

## Slide 12: Software Specification
Item | Description
Voice service | 8 Kbps EVRC encoded/decoded
 | emergency calls that can be configured by configuration software
 | Supplementary services: caller number identification presentation, call transfer, call forwarding, call waiting, call hold and three-way calling
 | Voice privacy during a call
Call records | Can query 20 received/missed calls, as well as 100 dialed calls. the number of new call displayed.
Phone Book | Max 500 contacts, and 10 groups
SMS | The memory is shared by the inbox, outbox, and draft, saving up to 100 messages; support predefined messages; Up to 160 English characters.
Utilities | Alarm Clock, Games, Calendar, Calculator, Stopwatch, World Time.
Tone options | 10 12-Polyphonic Ring tones

## Slide 13: Software Specification
Item | Description
Dialing | Hot-key support.
 | Supports to dial out the numbers in the calling records.
ISD/STD call lock | Supports code lock on ISD/STD
Volume adjustment | Conversation volume (level 1 to 4)
 | Ring volume (level 1 to 4)
Public CDMA WLL | Supports the reverse polarity billing and pulse billing information delivered by the network. With an accounter, the information related to the reverse polarity billing and pulse billing can be displayed on the FWT.

## Slide 14: Software Specification
Item | Description
Backlight | Provide backlight on LCD and keypad
PC Fax | Supporting PC Fax
Data service | High speed data service up to 153.6Kbps

## Slide 15
Contents
Chapter 1 Product Overview
Chapter 2 Technical Specification
Chapter 3 Functions Instruction
Chapter 4 Maintenance and Guide

## Slide 16: Functions Instruction
Voice service
  Voice service adopts 8kbps EVRC encoding/decoding
  Supports emergency calls, and the default emergency call numbers are 110, 112, 120, 119, 122, 911 and 999. You can configure another six emergency call numbers on the FWT by using the configuration software.
  Supports supplementary services: caller number identification presentation, call transfer, call forwarding, call waiting, call hold and three-way calling.
  Note：Consult local operator for subscribing to the supplementary services.

## Slide 17: Functions Instruction
Phonebook
        The FWP provides a phone book of large capacity. You can save up to 500 contacts to the FWP.
        You can save the call records either in the FWP.
        You can easily classify the contact in the phone book into groups such as Family, colleague, and Friends. This function facilitates the management and query of the phone book.

## Slide 18: Functions Instruction
SMS
Supports sending and receiving text short messages, and provides common phrases and message groups.
The message groups and the FWP groups are independent.
In the ROM-UIM mode, the FWP can save up to 100 messages. The inbox ,outbox and draft share the memory.
The FWP provides 10 message templates.
A message can be sent to more than one person at the same time (up to 10).
You can view, read and send message during a call.
The FWP supports the auto-save and auto-delete functions.

## Slide 19: Functions Instruction
Data service：
The FWT can transmit packet-switched data services at the rate of up to 153.6kbps/153.6kbps (uplink/downlink). To implement transmission of packet-switched data services, install the dedicated USB driver of the terminal and the relevant Modem driver on the PC, and then dial the access number “#777”, and enter MDN number as username and password.
Please refer to <CLASSIC2258 FWP Data Service User Manual> for Classic 2258 data service guideline.
USB driver and manual is available in ‘Huawei Classic 2258 USB Data Cable Driver & Manual.zip’.

## Slide 20
Usage of PC fax
Functions Instruction
The FWT supports to transmit circuit-switched data services at a rate of up to 14.4kbps, including PC fax services. Different services have different operation modes. For details, refer to the FWP Data Service User Manual.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21
Contents
Chapter 1 Product Overview
Chapter 2 Technical Specification
Chapter 3 Functions Instruction
Chapter 4 Maintanence and Guide

## Slide 22: Chapter 4 Maintenance and guide
Software upgrade guide
Normal problem solution
Major Spare Parts List

## Slide 23: Software upgrade Preparation
Huawei FWT Maintenance Tool v3.0 Available on Huawei CDMA Terminal Software CD(2006 Sep)
DB9 serial port data cable Part Code: 4043826
ETS2208 Reliance bin file: File name: ETS2258 V100R001B103sp28.zip Version: V100R001B103sp28 Version displayed on FWT Maintenance Tool v3.0: 202.11.03.103sp08

## Slide 24: Software upgrade guide
There are two modes of software upgrade
Normal Download: Normal software upgrade for the terminal. The terminal can power on normally.
Force download: The terminal can not power no normally. You can try to use force download.
And pay attention that: the phone need to power on and make sure the battery is full (or with power supply).

## Slide 25: Software upgrade guide—Normal download
Step1: Run the “FWT Maintenance Tool” and configure port and speed as showing in the picture.

## Slide 26: Software upgrade guide—Normal download
Step2: Choose the software and download.
Choose
APP file
Start upgrade
NOTE: APP file, the current version is WL3TAPB21003_UPDATE.APP

## Slide 27: Software upgrade guide—Normal download
After the upgrade process is done, the FWP will automatically reboot;
After reboot, check the version shown in FWT Maintenance Tool; Software Version display: SW Ver: 202.11.03.103sp08 Hardware Version display: HW Ver: WL71PIPU

## Slide 28: Software upgrade guide—Force download
If normal upgrade fails, you need to perform force download;
If the FWP power off or disconnected, you need to perform force download;.
The FWP can not power on normally, you can try force download;
STEPS:
Step 1: Connect the FWP with serial cable to the computer, and launch FWT Maintenance Tool;
Step 2: Configure the port and the rate , choose the software as normal download.
Step3 : Click “Forcedly download”. Then power off the terminal and power on it again. The downloading process will go on.
Remark:
The software will prompt whether the force download is successful.
Do not disconnect the data cable or power off in the progress of either normal download or forcedly download.
After the download is successful, the terminal will automatically reboot and the new software will take effect.

## Slide 29: Normal problem solution
Display problem
No charging problem
Power on problem
Key pad problem
Call problem
Handset free problem

## Slide 30: Display problem
Display problem
Describe: The handset showing no display, Segments missing, display intermittent or black display.
Solution: As this problem happened, you also can switch on the phone, the problem only with LCD or software.
Check the LCD line and re-solder the LCD, clear the connect interface.
Replace the LCD if you confirm it get faulty.
Upgrade the software for the black display problem.

## Slide 31: Display problem
LCD connector pins
LCD Backlight
LCD connector pins
LCD

## Slide 32: No charging problem
No charging problem
Describe: The charger can not charging the battery. After long time charging, also get low battery.
Solution: Before do the repairing, you need to confirm which part is faulty.
Connect the charger to power supply and check the output voltage with multimeter. It showed be 12V.
Then check the power connector, fuse, Q301 and replace the faulty one.
Otherwise check the main board and replace it if can not repair it.

## Slide 33: Power on problem
Power on problem
Describe: Can not power on or after power no get dead.
Solution: Each part have problem can cause this problem. We can find some normal problem can repair in the ASC.
Check charger and battery, make sure power supply no problem.
Check the power connector, fuse, Q301 are OK.
Check the power management part, make sure no chip has been brunt or lost.
Upgrade software for dead case. (Maybe need to do the force upgrade).

## Slide 34: Power on problem
Connector
Power
connector
Fuse
Q301: power circuit

## Slide 35: Key pad problem
Key pad problem
Describe: key pad is not working or display wrong number when you press.
Solution: If one a few key not working, you can clear the pad or check the metal; if a line or a row is not working, maybe main board problem.
Clear the keypad or upgrade software.
Check the metal dome and main board.
Replace main board.

## Slide 36: Call problem
Call problem
Describe: can not hear the voice, or can not make a call, or can not send out the voice.
Solution: Call problem is related to MIC, speaker, audio circuit, and RF part. But confirm account no problem.
Check MIC, speaker and handset (MIC and speaker is there).
Check the audio circuit and confirm there is no burnt on main board.
Then maybe RF part problem, Need to replace main board.

## Slide 37: Handset free problem
Handset free problem
Describe: can not hear voice or can not send out voice, but can make dial out and receive call.
Solution:
Check MIC and speaker. Or replace one and test.
Check audio chip. Make sure is power supply is ok and no burnt there. Tested the power supply of audio chip and ground, if the value is less then 900, some place is short. Maybe audio chip or PA.
Replace main board.

## Slide 38: Handset free problem
Speaker and audio circuit
Speaker
Handset line
Audio amplifier chip

## Slide 39: ETS2258 Main Spare Parts List
SN | Part number | Description
1 | 03020DVR | ETS2258 Reliance Main board
2 | 23040034 | ETS2258 LCD Module, Graphics 128*64 ,STN
3 | 22050045 | Microphone -RoHS
4 | 22020045 | Speaker
5 | 24020480 | battery（3.6V 1.0Ah）（P）
6 | 02130642 | New External Power Supply（190V-300V Phone Europe Style）
7 | 27160056 | Omni-Antenna-1.7(824~849)/2.0(869~894)
8 | 14190002 | Power Connector
9 | 04050038 | RF cable(0.15m TNC50SF )

## Slide 40: Usage Notice
1. Do not leave your FWT, battery, or power adapter in a high-temperature place or use them in a place with flammable gas. Otherwise, malfunction of the products, fire, or explosion may result.
2. Because FWT needs to eliminate heat during working, put the FWT and the power supply in a ventilated and shadowy place. Never airproof the FWT or put something on it or place it near water, fire as well as inflammable and explosive materials.
3. Before cleaning FWT, please turn off the FWT, and then disconnect the power supply and take out the battery. Before moving FWT, please disconnect the external power supply.
4. Do not subject your FWT, battery, and power adapter to serious collision or shock. Otherwise, battery leakage, FWT malfunction, overheat, fire, or explosion may result.

## Slide 41: Usage Notice
5. When lightning, if you use the power adapter, please turn off the FWT and disconnect the power adapter from external power supply. If outdoor antenna is used, please turn off the FWT and do not touch the interface between FWT and antenna.
6. Do not touch the antenna when a call is going on. Touching the antenna may affect call quality and cause the FWT to operate at a power level higher than needed.
7. The network signal condition will directly affect the quality and stability of the call. Consequently, you should place FWT in a place where it can receive network signal well. Do not put FWT in a building with an iron or metal roof. The distance between FWT and other metal materials (such as metal brackets or metal doors and windows) should be greater than 25cm and the distance between FWTs should be greater than 30cm.

## Slide 42: Usage Notice
8. Disconnect the power adapter and take out the spare battery when FWT is not used for a long time.
9.Notice on usage of the spare battery:
1). Charging duration should exceed 8 hours at the fist time.
2). Afterwards, it should up to 4 ～6 hours at least till the charging indicator on the LCD doesn’t flash.
3). If the charging has been interrupted, please discharge it first and then recharge it

## Slide 43: Usage Notice
4). If the network signal is not good ,please move the FWT to another place better in signal.
5). Don’t charge it frequently. You’d better take it out if external power works . Which prolongs its life-span and improves its stand-by duration. (It only can be charged 500 times)

## Slide 44: FAQ

## Slide 45
Thank You！
http://mobile.huawei.com