## Slide 1
C506 Product Knowledge Training
Feb.2007

## Slide 2
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 3: C506 Product Overview
Appearance
Model Name: C506

## Slide 4: C506 Product Overview
Appearance

## Slide 5: C506 Product Overview
Appearance

## Slide 6: C506 Product Overview
Main Features
Color display with 65 K CSTN
SMS
Smart English Input Mode
Wireless data service
Abundant applications
Caller ID display
Large capacity phone book
SMS groups and phone book groups
Type-ahead for words and phrases
Shortcut key function
Supplementary services
Secondary dial tone in DTMF
Light weight and flimsiness

## Slide 7: C506 Product Overview
Physical specifications
Item |  | Index
Dimensions (H x W x D) |  | 77.8 mm x 42.5mm x 20 .5mm (without antenna)
Weight |  | < 85 g (with battery)
Form |  | Flip
Antenna |  | External
UIM |  | R-UIM support for TATA
Battery | 550 mAh Li-ion | Stand-by time: 120 hours (Depending on network situation) Talk time: 2 hours (Depending on network situation)
 | 820 mAh Li-ion | Stand-by time: 180 hours (Depending on network situation) Talk time: 3 hours (Depending on network situation)

## Slide 8: C506 Product Overview
Item |  | Index
Display | Pixel | 128 x 96
 | LCD type | 65k CSTN
Interface | Charger interface | 24 pin
 | Data cable interface | 24 pin
 | Headset jack | 2.5mm

## Slide 9: C506 Product Overview
Performance specifications
Item | Index
Protocol | IS-95 & CDMA 2000 1X
Frequency band | Tx: 824 MHz – 849 MHz Rx: 869 MHz – 894 MHz
Polyphonic ringer | 16
Voice rate | 8K EVRC
Language supported | Supports English and Hindi.
Technical specifications
Item | Index
Protocol | IS-95 & CDMA 2000 1X
Performance | RF: 3GPP2 C.S0011-A (EIA/TIA98D) OTAPA & OTASP: Comply with the performance standards in TIA/EIA/IS-683

## Slide 10
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 11: C506 General Functions
Functions
SMS
Voice service
Date service
Phone book
Shortcut key
Polyphonic ringer
Applications
OTASP/OTAPA
Security
Supplement services
UTK function
BREW Applications download Function

## Slide 12: C506 General Functions
SMS
C506 can send and receive text short messages, and provide predefined text messages and group sending. The short message groups and the phone book groups are independent.
The handset memory can hold up to 100 messages. The inbox and outbox share the same memory.
With R-UIM, the number of messages saved to the UIM card depends on its capacity. In addition, you can save up to 100 messages to the phone memory.

## Slide 13: C506 General Functions
Data service
C506 support CDMA 2000 1X Packet Data Services at speeds up to 153.6 kbps for both Uplink and Downlink.
Data Modem ：
    Set the CDMA2000 1X high-speed data transmission rate at your phone;

## Slide 14: C506 General Functions
Data Service
C506 can be used as a wireless data modem, which allow you to benefit from surfer on internet at any time;
Set the CDMA2000 1X high-speed data transmission rate at your phone.
  Press Menu, and then select Settings/Data modem/High speed 1X data.
  Press for choose high-speed or low-speed data rate.
  Press Select to confirm the selection.
2. Insert to USB port and install driver;
Manual setup a connection in control panel;
Select the right modem port;
Connection setting: (TATA Indicom connection)
Dial-up: #777 Username: internet Password: internet
6. CONNECT TO SURF

## Slide 15: C506 General Functions
Phone Book
C506 provides you with a phone book of large capacity. The large-capacity phonebook can store up to 700 entries, the phone memory, 500 entries, and UIM card, 200 entries.
You can save the records either in the phone or in the UIM. You can also copy the records between the phone and the UIM.
Besides, C506 supports group function in the phone book. You can easily classify the entries in the phone book into groups such as Family, Business, and Friends. This function facilitates the management and query of the phone book.

## Slide 16: C506 General Functions
Shortcut Key
C506 offers the shortcut key function. You can press one key to speed-dial a preset number, mute the voice, lock the keypad and so on.
Polyphonic Ringer
There are twenty pieces of sixteen polyphonic ringers in the C506. It will bring great music to your communication life.
Applications
C506 presents several applications, including alarm, calculator, calendar, game, stopwatch, currency convert and world time.
Supplementary Services
C506 provides several supplementary services, including call waiting, call forwarding, and three-way calling.

## Slide 17: C506 General Functions
OTASP
C506 shall support TIA/EIA/IS-683A capabilities for Over The Air Service Provisioning (OTASP). Subscribers will be able to initiate initial programming of Number Assignment Modules, data options, operating parameters etc. Generation and verification of Authentication Key, programming of preferred roaming lists are available.
OTAPA
C506 shall support TIA/EIA/IS-683A capabilities for Over The Air Parameter Administration (OTAPA). Network will be able to initiate update, individual Number Assignment Modules, data options, operating parameters, and service provider specific or manufacturer specific parameters. Update of preferred roaming list, generation of Authentication Key, addition and update of parameters for future services will be available.

## Slide 18: C506 General Functions
Security Settings
Setting Phone Lock
This function prevents unauthorized use of the phone after the phone is stolen or the R-UIM card is changed. This function is not activated upon purchase. You can change the default phone lock code "0000" into any code of four to eight digits.
Press Menu to select Settings/Security/Phone lock.
Enter the correct phone lock code and press Ok.
Select one of the following options:
  On/Off: Activate/Deactivate the phone Lock.
  Change code: Enter a new phone lock code. After you enter the new phone
  lock code, the phone requests you to enter again to confirm the new code.

## Slide 19: C506 General Functions
Setting PIN Lock
If the PIN Lock function is activated, your phone displays the message Input PIN: when powered on. To use the phone, you need to enter the correct PIN and then press Ok.
If you enter a wrong PIN for three successive times, your R-UIM card is locked. To unlock the R-UIM card, you need to enter the correct PUK code.
Press Menu to select Settings/Security/PIN lock.
Enter the correct PIN and press Ok.
Select one of the following options:
  On/off: Activate/Deactivate the PIN Lock.
  Change code: Enter a new PIN (4 to 8 digits).

## Slide 20: C506 General Functions
Setting PIN Code
You can use the PUK code to change the locked PIN. The PUK code also comes with your R-UIM card. If you do not have the PUK or you lose or forget it, please consult your service provider.
If you enter a wrong PUK code for ten successive times, your R-UIM card is destroyed. In this case, you need to contact with your service provider to replace the R-UIM card.
Enter the correct PUK code and press Ok.
Enter a new PIN and press Ok.
Re-enter the PIN and press Ok.
Restoring Factory Settings
Press Menu to select Settings/Restore factory settings.
Enter the correct phone code and press Ok.

## Slide 21: C506 General Functions
UTK Function
C506 allows the UTK function through which you can interact with applications in the UIM supplied by the network provider. The network provider may prefabricate some increment services in R-UIM. Handset and R-UIM card can found user operation interface, the interface can receive user dictate, perform application on R-UIM card.
BREW Applications download Function
C506 supports the Application Manager and Download Center (Mobile Shop) by the network provider. The Application Manager may display, browse and download applications from network provider’s server. For the applications, It can provide delete, upgrade, purchase, disable, restore functions. You may choose your favorite services by downloading and perform.

## Slide 22
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 23: C506 Upgrade Software
Naming of the Host Software version
Naming of the Download Software version
Tools for upgrade
Download software-downloading methods
Downloading the APP code through the serial port
Downloading APP Code Using USB Port

## Slide 24: C506 Upgrade Software
Naming of the Host Software version
C506 handset host soft versions are named as: C506V100R001CxxBxxxSPxxx
Cxx is the code number of customer.
Bxxx is the main host soft version number.
SPxxx is the version number of package.
For TATA-C506, Please choose the file as following:
C506V100R001C02B113-TATA
APP: “HWC506MT05UpdateApp”

## Slide 25: C506 Upgrade Software
Naming of the Download Software version
HUAWEI Download Software is the software used for C506 host software download.
For TATA-C506, please use the following Download software:
“HC1DLOD1C01B106SP01”

## Slide 26: C506 Upgrade Software
Tools for upgrade：
  Data cable：there are two type of data cable USB-port data cable and serial-port data cable. But in ASC we use the serial-port data cable for upgrade software.
  PC：for run the download software with serial port or USB port.
  Host Software: Its bin file or app file which will given by huawei.
  Handset: keep battery capacity full or the battery bar is more than two.

## Slide 27: C506 Upgrade Software
Download software-downloading methods ：
The Download Software provides the following two downloading methods.
  Normal Downloading ：This method is applicable to the software upgrade when the handset is in normal power-on status.
  Forced Downloading ：This method is applicable when the handset cannot be powered on normally.

## Slide 28: C506 Upgrade Software
Downloading the APP code through the serial port
Normal Downloading
If the handset operates normally, you can download the APP code using the normal downloading procedure, proceed as follows:
Step1: Start this software.
When you start the software, the system displays the [Input Login Password] dialog box if you enable login password. To log in to the software, you have to enter the valid password. If you do not enable the login password, the system does not display the dialog box, and you can directly log in to the software.

## Slide 29: C506 Upgrade Software
The default password is C300.znkl
Step2: Click "System Configuration" on the "Tool List".
Step3: Set the port number.
On the [Communication Configuration] window, to set the port number used for the communication between PC and handset.

## Slide 30: C506 Upgrade Software
Step4: Click "Download Tool" on the "Tool List".
Step5: Click <Browse> and select the APP file.
Step6: Click<Open> and the software displays the information about the parameter packet as shown in Figure 1-1.
Step7: Press the “Download” key. The software automatically backs up the important data.
After the completion of the data backup, the handset is switched to the downloading mode and starts downloading the APP code as shown in Figure 1-2. The handset screen displays the message "Downloading indication".

## Slide 31: C506 Upgrade Software
Figure 1-1 Parameter packet information
Figure 1-2 Downloading APP code
*NOTE:
Do not modify the configuration file or any file in the folder Configuration File. Otherwise, file verification will result in failure.

## Slide 32: C506 Upgrade Software
After the APP code is downloaded, the handset restarts automatically. The download tool begins to restore the backup data and then add some files and data necessary for the APP code version as shown in Figure 1-3.
Step8: The downloading is completed. As showing in figure 1-4.

## Slide 33: C506 Upgrade Software
Figure 1-3 Restore data and add some files and data
Figure 1-4 Downloading is complete

## Slide 34: C506 Upgrade Software
Caution：
If errors such as power failure or cable disconnection occur during the downloading process and lead to the downloading failure, use the forced downloading instead. After the APP code is downloaded, the download tool begin to restore the backup data, you do not need to calibrate the RF parameters.
No intervention is required for the whole downloading process. But if the data backup, restoration, or addition of resource files or data fails, a dialog box will appears, requiring you to select <Stop>, <Retry> or <Neglect> . It is recommended that you select <Retry>. If the operation fails after several retries, select <Neglect>. However, the handset may fail to operate normally. Do not select <Stop> unless necessary. Selecting <Stop> may result in malfunction of the handset.

## Slide 35: C506 Upgrade Software
Forced downloading
To download the APP code using the forced downloading method, proceed as follows:
Step1: Start downloading software.
Step2: Click "System Configuration" on the "Tool List".
Step3: Set the port number as normal download.
Step4: Power off the handset.
Step5: Click "Download Tool" on the "Tool List".
Step6: Click<Browse> and select the APP file.
Note：
Do not modify the APP file or any file in the folder APP File. Otherwise, file verification will result in failure.

## Slide 36: C506 Upgrade Software
Step7: Press the numeric key "5" and "Power" key on the handset at the same time to enter the forced downloading status. And the handset screen displays the message "Forced downloading". Click <Download> to start the forced downloading.
Step8: If the forced downloading is not caused by failure in normal downloading, Figure 1-5 is displayed. Click <Cancel> to stop the downloading. Otherwise, forced downloading is started.
Figure 1-5 Continue to force download

## Slide 37: C506 Upgrade Software
After the APP code is downloaded, the Download Software will download some additional resource files and data required by the handset according to the configuration file.
The whole downloading process ends.
Caution：
After the forced downloading, you need to calibrate the RF parameters before the handset can operate normally.
During the Forced Downloading, you cannot back up or restore the user data or system data of the handset. Any attempt of data backup or restoration may lead to unavailability of some functions of the handset.
If errors such as power failure or cable disconnection occur during the downloading process and lead to the downloading failure, repeat the forced downloading procedure

## Slide 38: C506 Upgrade Software
NOTE- Download with serial cable
  Must set handset to the correct data port, keypad input: ##745698 enter [Engineer Mode->Port Set->Serial].
  Do not modify the configuration file or any file in the folder Configuration File. Otherwise, file verification will result in failure.
  Keep battery capacity more than 2 grad display on the LCD banner.
  If errors such as power failure or cable disconnection occur during the downloading process and lead to the downloading failure, use the forced downloading instead. After the APP code is downloaded, the download tool begin to restore the backup data, you do not need to calibrate the RF parameters.

## Slide 39: C506 Upgrade Software
Downloading APP Code Using USB Port
The downloading procedure is the same as that through the serial port except the Communication Configuration.

## Slide 40: C506 Upgrade Software
NOTE- Download with USB cable :
USB download also support two methods :normal downloading and forced downloading.
Install the driver under the directory where the USB driver delivered with this software is located.
Set the number of the port used for communications to the one displayed in [Device Manager] [Ports(COM&LPT)]

## Slide 41: C506 Upgrade Software
Prompts
During the above operations, the download software displays a number of prompts in the message list as shown in the table below to indicate the current operations or their corresponding operating status.
No. | Prompt | Remarks
1 | Configuration file check sum failed | Contact the configuration file provider.
2 | Configuration file check sum OK | --
3 | Backuping EFS files… | Includes the system file of the handset regarding phonebook and SMS; Depends on version.
4 | Backuping Nv data… | Mainly includes key parameter of handset

## Slide 42: C506 Upgrade Software
5 | Switching to download mode! | Prepares to download APP code
6 | Trying to get ESN ... | This message is displayed after failure in getting the ESN of the handset. The software can attempt to get the ESN for up to ten times.
7 | Could NOT get ESN! | Fails even after attempts for another ten times
8 | ERROR: Mismatched ESN! | Probably caused by the replaced handset during the operation
9 | ERROR: Invalid mobile phone parameter file, THIS PHONE MAY BE DESTROYED! | This message is displayed when the data fails to be backed up and the software is upgraded through forced downloading. In this case, the data is not restored after the APP is downloaded.

## Slide 43: C506 Upgrade Software
10 | Force download! | Starts forced download anyway
11 | Downloading file: | --
12 | Rebooting | Restarting handset
13 | ERROR: Erase flash error! | Probably caused by power failure of the handset or loose connection of the data cable
14 | Skip downloading application! | The APP file is not added to the configuration file. Data processing instead of software upgrade is conducted.
15 | Creating EFS files Adding EFS file: … | --
16 | Restoring EFS files ... | --
17 | Restoring EFS files ... done! | --
18 | Restoring NV Data ... | Includes some system parameters of handset

## Slide 44: C506 Upgrade Software
19 | Restoring NV Data ...done! | --
20 | ERROR: Open file …… | This file might not exist or is being used by other software.
21 | ERROR: SPC code error! | The SPC code in the configuration file is not consistent with that of the handset. Contact the configuration file provider.
22 | Trying write NV | --
23 | Connecting to board ... | --
24 | Unsupported degrade! | Depends on version
25 | Found ERROR! | Stop the upgrade procedure upon any error found.
26 | Done! | Do not disconnect the handset from the PC except when the upgrade failure is caused by the error found.
27 | Reading phonebook file of the handset. | Exported phonebook file from the handset to PC

## Slide 45: C506 Upgrade Software
28 | Writing phonebook of the handset. | Imported effective phonebook records currently displayed into the handset
29 | Fails to export EFS files! please check whether the mobile startups correctly! please check whether the mobile is connected with PC! please check whether the port is occupied by other program! | Exception during exporting phonebook file from the handset to PC
30 | To write phonebook is ok ! | Complete to replace phonebook records of the handset with current records displayed in the PC software
31 | To save record file: is Ok! | Complete to save phonebook records currently displayed as the local record CSV file
32 | Idle State! | No operations for phonebook tool
33 | Fails to open serial COM! please check whether the port is occupied by other program! please check whether the port is set correctly! | Exceptions that PC could not connect with the handset

## Slide 46
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 47: C506 Engineer Mode
C506 Engineer Mode－Enter Debug Menu
Keypad command | Description
##745698 | Maintenance test menu (for ASC)
##258741 | Restore factory setting
*#06# | Query ESN
The engineer mode of C506 is mostly like C2205, only major difference is under maintenance test menu, we can select port for software download

## Slide 48
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 49: C506 Assemble & Disassemble
Please refer to this document：

## Slide 50: C506 Assemble & Disassemble
Over view the main board
Over view the LCD

## Slide 51
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 52: Troubleshooting
Fault 1: No outgoing call
Symptom: The call originator can hear the opposite party, but the opposite party cannot hear the voice of call originator.
Troubleshooting: Carry out the following procedure. If the problem persists, proceed with the next step.
Check whether the software version is the latest version. If not, upgrade it to the latest version.
Use the earphone to test whether call is sent out. If it is, the microphone may be faulty.
Failure outgoing call is usually caused by faulty microphone. Use a multimeter to measure the on-line resistance of the MIC. If the deviation larger than 5%, replace the MIC .
Replace the main board.

## Slide 53: Troubleshooting
Fault 2: No incoming call
Symptom: The call originator cannot hear the opposite party, but the opposite party can hear the voice of call originator.
Troubleshooting:
Use the faulty handset to make a call and stay in the conversation status. Use a side key to adjust the volume to the maximum extent.
No incoming call is mostly caused by faulty microphone. Use a multimeter to measure the on-line resistance of the microphone the resistance value should be approximately 32 ohms. If the deviation exceeds 2 ohms, replace the microphone.
Check whether there is open joint on the FPC. Check the CON600 (#8,#10) and J901 (#4,#5) are connected .if yes ,then replace the FPC .
Replace the main board.

## Slide 54: Troubleshooting
Fault 2: Not power on
Symptom: The handset fails to power on when the battery is loaded or the charger is connected.
Troubleshooting:
Apply a power supply to the handset to see whether it can be powered on. If it can, replace the battery. Or replace a normal battery to see whether the handset can be powered on. If it can, replace the battery.
If the handset still fails to power on, apply a DC power supply to see whether the handset can be powered on (the voltage of the DC power supply is set to 3.8V).
  If no power-on current exists, check whether the battery connector is soldered improperly. Weld it again, or clean the keypad;
  If the current is tiny, the power supply part is faulty or the crystal oscillator is faulty. Replace the main board.

## Slide 55: Troubleshooting
Fault 2: Not power on (continue)
  If the current falls within 60~200 MA, the CPU may be welded improperly, or the flash is faulty, or the software is faulty. Replace the main board.
  If the current is huge, and short-circuit exists, observe the main board components to see whether they are damaged or corroded. Then detect is there any place heated by touching, If the problem is in main board, replace the main board.

## Slide 56: Troubleshooting
Fault 4: No signal
Symptom: No signal symbols or time in the signal coverage area.
Troubleshooting:
Disassemble the mobile phone, and observe the antenna contact part and the main board part to see whether they are damaged obviously (e.g., component detachment). If they are damaged, replace the components.
Replace the main board.

## Slide 57: Troubleshooting
Fault 5: Keypad malfunction
Symptom: One or more keys does not work after powering on the handset.
Troubleshooting: The failure of keys may be caused by: oxidized key film; disconnection of PCB.
Clean the keypad .
Replace the metal key film.
Replace the main board.

## Slide 58: Troubleshooting
Fault 6: No display
Symptom: The screen displays nothing when the handset is power on.
Troubleshooting: The fault of no display is caused by: LCD fault; FPC fault ;software fault or main board fault.
Replace a new LCM (with FPC ),
Check the J901.If it dry welding, re-soldering it .
Replace the main board.

## Slide 59: Troubleshooting
Fault 7: No ringtones
Symptom: In the menu setup, enable the tone functions, and set the tone to the maximum volume, but no tone can be heard. No tone is sounded when a call comes in, and no music is heard after powering on the machine.
Troubleshooting:
1. Recover the factory settings to preclude the setting problem.
2. Replace a good folder. If it works normal ,then we can detect the main board is good. Otherwise Replace the main board .
3. Check the buzzer. Use a multimeter to measure the resistance of the buzzer on the line. The normal value is approximately 8 ohms. If the deviation exceeds 1 ohm, replace the buzzer .
4. Replace the FPC .

## Slide 60: Troubleshooting
Fault 8: Not charging
Symptom: Load the battery and Insert the charger. The battery scroll bar remains still, and the battery fails to charge. Then, connect the charger, and it displays charging in progress. But actually no charging is effective.
Troubleshooting: Replace the battery or charger with a normal one to check whether the fault lies in the battery or charger or the main board.
Use a normal battery and charger to test the charging of the faulty handsets. If charging is normal, replace the battery or charger.
Failure of charging is mostly caused by false weld of the data connector. Weld the data connector or replace it, and the problem will disappear. In addition, false weld or breakage of the charging circuit component on the main board may cause failure of charging.
Replace the main board.

## Slide 61: Troubleshooting
Fault 9: No vibration
Symptom: Set the handset to the vibration status, and no vibration occurs.
Troubleshooting: This fault may be caused by faulty motor of vibration, or faulty circuit related to circuit.
View the ringing mode to see whether it is “vibration” or “vibration + ringing tone”. If not, set it to “vibration” or “vibration + ringing tone” .
Disassemble the handset. Assemble the motor again to see whether it works normally.
Detach the motor. Apply a 2.5V voltage to both ends of the motor to see whether it vibrates. If it does not vibrate, replace the motor.
Replace the FPC . If the problem persist ,replace the main board.

## Slide 62
Faulty 10: LCD get blue
Problem: Some times the LCD get blue and there is no display.
Analyze: The LCD line is not solder properly, So we can resolder the line first. Otherwise we can change a new LCD for a try.
Resolder this line
Troubleshooting

## Slide 63
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 64: C506 FAQ
Battery and Charger
Q: How to activate the battery?
A: When delivered from the factory, the battery contains about one-third battery charge. After purchasing a new handset, please make sure that the battery is charged only after it is used up so that the handset turns off automatically, and that the battery is charged continuously for eight hours during the first three charging. In this way, the battery can be activated.
Q: How long does it take to charge the battery?
A: When using a 550mAh battery, charge the battery for about two hours;
When using an 820mAh battery, charge the battery for about three hours.

## Slide 65: C506 FAQ
Q: How to judge whether the charging is finished?
A: After the charging is finished:
  The seven-color lamp on the cover turns green from red during the charging.
  The battery icon displays full bars and blinks.
Q: How to plug in and unplug the charger?
A: Please squeeze the two latches on both sides of the charger to plug in or unplug it. Incorrect operation may result in damage to the charge interface of the handset or the interface of the charger.

## Slide 66: C506 FAQ
Voice Service
Q: In what cases can I make emergency calls?
A: The UIM card is not inserted;
The handset is locked or the UIM card is locked;
  The keypad has been locked.
[Note] To make an emergency call, the handset must be turned on and in a service area with adequate signal strength.

## Slide 67: C506 FAQ
Q: How to dial the telephone numbers with extension numbers?
A: You can dial an extension number in the following two modes:
After inputting an operator number, press the up key to input “P” between the operator number and the extension number.
After inputting an operator number, press the down key to input “T” between the operator number and the extension number.
Data Service
Q: What functions does the data service of C506 involve?
A: Data MODEM function, PC fax function and asynchronous data communication function.

## Slide 68: C506 FAQ
Q: Can I answer a call when using the data service?
A: You can answer a call normally when using the data service only when the network supports Voice Preferred and the call waiting function is available for your handset. Otherwise, you cannot answer the call when using the data service.
Q: Can I make a call when the handset is set to Fax/Data Reception Mode?
A: You can make calls or access the Internet when Fax/Data Reception Mode is set for receiving fax or data.

## Slide 69: C506 FAQ
Security
Q: What function does the phone lock fulfill?
A: The phone lock function can prevent the handset from being stolen or being used without your approval after the UIM card is replaced. When the phone lock function is enabled, you are required to enter the correct phone lock password each time the handset is turned on before you can use the handset normally.
Q: What is difference between the phone lock password and PIN?
A: The Personal Identification Number (PIN) lock function can prevent the UIM card service from being used without approval. You can use the handset after replacing the UIM card. The phone lock function can prevent the handset from being used without approval. If you fail to enter the correct phone lock password, you cannot use the handset normally even if you replace the UIM card.

## Slide 70
C506 Product Overview
C506 General Functions
C506 Upgrade Software
C506 Engineer Mode
C506 Assembly & Disassembly Guide
C506 Troubleshooting
C506 FAQ
C506 Spare Parts List
Course contents

## Slide 71: C506 Exploded View

## Slide 72: C506 Spare Parts List
SN | Part Code | Description
1 | 03020AYD | C506-Main board for service (General)
2 | 03028837 | C506-LCD Driver Board
3 | 03029167 | C506-FPC Board
4 | 23040030 | C506-LCD Module
5 | 24020401 | C506-Li-ion Battery (Blue)
6 | 24020370 | C506-Li-ion Battery (Red)
7 | 2130628 | C506-Travel Charger-European Plug
8 | 51660173 | C506-Flip Front Assy (blue)
9 | 51660065 | C506-Flip Front Assy (red)
10 | 51660174 | C506-Housing Bottom Assy (blue)
11 | 51660068 | C506-Housing Bottom Assy (red)
12 | 51660066 | C506-Flip Rear Assy
13 | 51660067 | C506-Housing Top Assy
14 | 51620114 | C506-Screw T5
15 | 51620085 | C506-Metal dome

## Slide 73: C506 Spare Parts List
16 | 51630100 | C506-Earphone Rubber
17 | 48020066 | C506-Lens Assy -TATA
18 | 51630104 | C506-Screw Cover Left
19 | 51630105 | C506-Screw Cover Right
20 | 51630106 | C506-Screw Cover Back
21 | 51640004 | C506-Hinge
22 | 51610078 | C506-Keypad(tata)
23 | 27160025 | C506-Antenna
24 | 22050024 | C506-Microphone
25 | 22020021 | C506-Speaker
26 | 22030008 | C506-Reciever
27 | 32050013 | C506-Vibration Motor
28 | 14240011 | C506-BTB Connector,Female-CON600
29 | 14240012 | C506-BTB Connector,Male-J2
30 | 14240024 | C506-SIM Socket-CON602
31 | 14240030 | C506-IO Connector-CON700

## Slide 74: C506 Spare Parts List
32 | 14240010 | C506-Earphone Connector-CON800
33 | 14240004 | C506-RF Switch-J101
34 | 13080008 | C506-Duplexer-U101
35 | 13010058 | C506-TX SAW FILTER-U102
36 | 47100048 | C506-Power Amplifier Module-U103
37 | 12070006 | C506-TCXO,19.2MHz-U105
38 | 39200018 | C506-RFR6122 RF-to-Baseband Receiver-U201
39 | 39200019 | C506-RFT6122 Baseband-to-RF Transmitter-U301
40 | 39200017 | C506-PM6610 Power Management-U400
41 | 39200004 | C506-MSM6025-U500
42 | 12020102 | C506-Crystal,32.768KHz-X400
43 | 12020109 | C506-Crystal,48MHz-X500
44 | 13010086 | C506-RX SAW FILTER-Z201
45 | 39080072 | C506-Audio Power Amplifier-U803
46 | 51650032 | C506-Disassemble-proof label (English)

## Slide 75
Thank You
www.huawei.com